- GENERAL

  - CONDITIONS SPECIFIED ELSEWHERE: SEDCTION 010000 – General Requirements.

  - SUBMIT SHOP DRAWINGS showing overall dimensions (width, height).

  - SUBMIT 3 copies of manufacturer’s owner’s manual, maintenance manual.

  - WARRANTY: Proposals submitted without the following written warranties will be considered non-responsive.

  - Door manufacturer shall provide with his bid a written 1 year warranty.

  - Door parts covered under the warranty shall include all components.

  - Door parts not covered under the warranty shall include: None.

  - In addition to all other warranties, the manufacturer shall warrant that the equipment will perform in a manner satisfactory to the Owner for a period of 12 months after date of installation. If Owner is not then satisfied with the performance of the equipment, the Owner may notify the manufacturer, and the manufacturer shall remove the equipment and refund the equipment purchase price to the Owner. This warranty shall be provided by the manufacturer in writing at the time of the bid.

- PART 2  -  PRODUCTS

  - Impact doors shall be Model 4800 as manufactured by Rite-Hite Door, Inc. or an approved substitute. Doors shall be sized by manufacturer to meet specific application requirements.

  - Impact doors shall be made for _____wide x _____high door opening(s).

  - Impact doors shall be 1-3/4” square steel tubular frame with high density foam core. Facing to be 1/8” ABS riveted to frame with black steel rivets, using foam tape.

  - Panels shall be suspended by through rivets in a one piece 11ga steel stile. Stile shall be welded to 1-5/16” diameter shaft.

  - Double pane 1/8” thick Lexan® vision panel shall be 24” high x full width of door panel, secured to frame with steel rivets and replaceable in the field.

  - Jamb mounted hardware shall provide a 180 degree opening consisting of 1-1/4” rise cam with needle bearing follower and lower pivot hinge, factory aligned and pinned.

  - Full perimeter gasketing shall be provided.

  - 35 oz. Hypalon® loop at header.

  - 35 oz. Hypalon on both leading edges filling a minimum 2- 1/2” safety gap.

  - PVC/Polyurethane stile mounted blade seal.

  - 35 oz Hypalon bottom blade air seal.

  - Flexible Hypalon covers for top hardware.

  - Lower hardware pivot hinge shall be enclosed with 10-1/4” high x 3/16” steel jamb guard.

  - Lower shaft shall be threaded for 5” steel spring which shall compensate for up to 10mph pressure with adjusting nut.

  - Lower 24” of door shall have 1/4” thick polyethylene tear drop bumpers installed with pre-threaded sleeves in frame and steel bolts and washers.

  - ABS facing shall be selected from manufacturers standard colors.

- PART 3  -  EXECUTION

  - INSTALLER shall examine the jamb conditions into which the Impact Door is to be installed and notify the A/E and Contractor in writing of any conditions detrimental to the proper and timely completion of the work.  Do not proceed with the work until unsatisfactory conditions have been corrected in a manner acceptable to the installer.

  - DOOR MANUFACTURER’S REPRESENTATIVE shall install the Impact Door in accordance with approved shop drawings and manufacturer’s recommendation.  Location of Impact Door shall be indicated on drawings.

  - ADJUST UNITS to operate smoothly.

  - AFTER INSTALLATION in complete, a representative of the manufacturer shall examine the installation and require that all adjustments to assure proper operation of the Impact Door has been made.  Before acceptance, a demonstration shall be conducted in the presence of the owner’s representative that all doors operate properly in every aspect.