Architectural Specifications

– Rite-Hite Doors’ Impact Door Model 3800 –

Section 08380

PART 1 - GENERAL								Page 1 of 2

  - CONDITIONS SPECIFIED ELSEWHERE: Section 010000-General Requirements

  - SUBMIT SHOP DRAWINGS showing overall dimensions (width, height).

  - SUBMIT a copy of manufacturer’s owner’s manual.

  - WARRANTY: Proposals submitted without the following written warranties will be 		considered non responsive.

  - Door manufacturer shall provide with his bid a written 1 year warranty.

  - Door parts covered under the warranty shall include all components.

  - Door parts not covered under the warranty shall include: Lubrication, seals, vision.

  - In addition to all other warranties, the manufacturer shall warrant that the equipment will perform in a manner satisfactory to the Owner for a period of 12 months after date of installation.  If Owner is not then satisfied with the performance of the equipment, the Owner may notify the manufacturer, and the manufacturer shall remove the equipment and refund the equipment purchase price to the Owner.  This warranty shall be provided by the manufacturer in writing at the time of the bid.

PART 2  -  PRODUCTS

2.1	Impact doors shall be Model 3800 as manufactured by Rite-Hite Door, Inc or an

approved substitute.  Doors shall be sized by manufacturer to meet specific application

requirements.

2.2	Impact doors shall be made for _____wide x _____high door opening(s).

2.3	Impact doors shall be 1/4” thick ABS panels.

2.4	Panels shall be suspended by through rivets in a one piece PVC stile.  Stile shall be

riveted to 1” diameter shaft.

2.5	Single pane 1/8” thick Lexan® vision panel shall be 11” x 16” in black flexible gasket, 		centered in the panel and replaceable in the field.

2.6	Jamb mounted hardware shall provide a 180 degree opening consisting of 3/4” rise cam

with needle bearing follower and lower pivot hinge, factory aligned and pinned.

PART 2  -  PRODUCTS (continued)						Page 2 of 2

2.7	ABS panel shall be selected from manufacturer’s standard colors.

PART 3  -  EXECUTION

3.1	INSTALLER shall examine the jamb conditions into which the Impact Door is to be installed and notify the A/E and Contractor in writing of any conditions detrimental to the proper and timely completion of the work.  Do not proceed with the work until unsatisfactory conditions have been corrected in a manner acceptable to the installer.

3.2	DOOR MANUFACTURER’S REPRESENTATIVE shall install the Impact Door in

accordance with approved shop drawings and manufacturer’s recommendation.

location of Impact Door shall be indicated on drawings.

3.3	ADJUST UNITS to operate smoothly.

3.4	AFTER INSTALLATION in complete, a representative of the manufacturer shall examine the installation and require that all adjustments to assure proper operation of the Impact Door has been made.  Before acceptance, a demonstration shall be conducted in the presence of the owner’s representative that all doors operate properly in every aspect.